COMP 315
Camera, projection and model view
Deshen Moodley
University of KwaZulu-Natal

---
Coordinate Systems
Coordinate Systems
- The units in points are determined by the application and are called object, world, model or problem coordinates
- Viewing specifications usually are also in object coordinates
- Eventually pixels will be produced in window coordinates
- OpenGL also uses some internal representations that usually are not visible to the application but are important in the shaders

---
OpenGL Camera
OpenGL Camera
- OpenGL places a camera at the origin in object space pointing in the negative z direction
- The default viewing volume
  is a box centered at the
  origin with sides of
  length 2, i.e. x, y & z values range
  from -1 to 1

---
Orthographic Viewing
Orthographic Viewing
In the default orthographic view, points are
projected forward along the z axis onto the
plane z=0
z=0
z=0

---
Transformations and Viewing
Transformations and Viewing
- The graphics system automatically transforms World (object) coordinates to screen coordinates
- In OpenGL, projection is carried out by a projection matrix (transformation)
- Transformation functions are also used for changes in coordinate systems
- Pre 3.0 OpenGL had a set of
transformation functions
which have been deprecated
Will look at these later

---
Viewports
Viewports
- Do not have use the entire window for the image: glViewport(x,y,w,h)
- Values in pixels (window coordinates)

---
Geometric primitives – outline shapes
Geometric primitives – outline shapes
- Points, lines & triangles are basic
- Other’s like quads, polygons are approximated using the basic primitives
- Outline shapes:

---
Geometric primitives – filled shapes
Geometric primitives – filled shapes
Polygon mode is used to create filled shapes
To generate a edge and the fill requires two renderings

---
Geometric primitives – filled shapes
Geometric primitives – filled shapes
Polygon mode is used to create filled shapes
To generate a edge and the fill requires two renderings

---
Colour
Colour
- Uses RGB colour space
- Is independent of display adapter/display device
- Specify a point on a unit RGB colour cube
- Float values along each side axis range from 0 – 1 -> (r, g, b)
- Examples
  - 1, 1, 1 -> white
  - 1, 0, 0 -> red
  - 0, 1, 0 -> green,
  - yellow ?
- To set the current colour use gl.glColor3f(r, g, b)

---
RGB color
RGB color
- Each color component is stored separately in the frame buffer
- Usually 8 bits per component in buffer
- Color values can range from 0.0 (none) to 1.0 (all) using floats or over the range from 0 to 255 using unsigned bytels

---
Smooth Color
Smooth Color
Default is smooth shading
  - OpenGL interpolates vertex colors across visible polygons
- Alternative is flat shading
  - Color of first vertex
determines fill color
  - Handle in shader

---
Program Structure
Program Structure
- Most OpenGL programs have a similar structure that consists of the following functions
- main():
  - glutInit initializes GLUT
  - glutInitWindowSize, glutInitWindowPosition,glutCreateWindow Creates a window at the specified position and size
  - glutDisplayFunc, glutReshapeFunc sets the display and reshape call back functions
  - glutMainLoop Enters an infinite processing loop
- initGL(): sets the state variables, viewing, attributes (called directly in main to group once off initial commands)
- display()- OpenGL statements to render objects
- reshape()- first repaint after component has been resized and when window first appears

---
Two dimension transformations
Two dimension transformations
Three general transformations
  - Translation - moves the world along the x,y,z axis
  - Rotation - rotates the world around the x,y,z axis
  - Scaling - magnifies or shrinks the world
- 3D case is a simple extension of 2D method for translation and scaling but more complicated for rotation
- OpenGL provides the following function for 3D transformations
  - Translation - glTranslate(x,y,z)
  - Scaling - glScale(x,y,z)
  - Rotation - glRotate(angle, x, y, z)
- See Nate Robbins Transformation tutor program

---
Translation -2D
Translation -2D

---
Translate example
Translate example
   glMatrixMode(GL_MODELVIEW); // To operate on Model-View matrix
   glLoadIdentity(); // Reset the model-view matrix
   glTranslatef(-0.5f, 0.4f, 0.0f); // Translate (x,y,z) left and up
   glBegin(GL_QUADS); // Each set of 4 vertices form a quad
      glColor3f(1.0f, 0.0f, 0.0f); // Red
      glVertex2f(-0.3f, -0.3f); // Define vertices in counter-clockwise	// (CCW) order
      glVertex2f( 0.3f, -0.3f); // so that the normal (front-face) is	// facing you
      glVertex2f( 0.3f, 0.3f);
      glVertex2f(-0.3f, 0.3f);
   glEnd();

---
Rotation example
Rotation example
 glRotatef(180.0f, 0.0f, 0.0f, 1.0f); // Rotate 180 degrees around the x
// axis
 glBegin(GL_TRIANGLES); // Each set of 3 vertices form a triangle
      glColor3f(1.0f, 0.0f, 0.0f); // Red
      glVertex2f(-0.3f, -0.2f);
      glColor3f(0.0f, 1.0f, 0.0f); // Green
      glVertex2f( 0.3f, -0.2f);
      glColor3f(0.0f, 0.0f, 1.0f); // Blue
      glVertex2f( 0.0f, 0.3f);
   glEnd();

---
Transformation example
Transformation example
Work through GL04ModelTransform.cpp program in the tutorial to gain an understanding of transformations on the world
Check Howard’s OpenGL Tutorial and Reference, page 49 to gain a better understanding of the OpenGL transformation commands

---
Rotation
Rotation
θ

---
OpenGL tutorial
OpenGL tutorial
You should work your way through the following tutorials to familiarise yourself with OpenGL in C++
https://www3.ntu.edu.sg/home/ehchua/programming/opengl/CG_Introduction.html
Toby Howard's tutorial and reference guide on the course website